TEMIZ EVREN
acceptance criteria for - R3/R12 to R1 - recovery of
scrap plastics EWC 19.12.04 // materials code 99180xx
Rev 183

CRITERIA	ACCEPTABLE	NOT ACCEPTABLE
EWC CODES	19.12.04	ALL THE OTHER EWC CODES
MATERIALS INCLUDED	SELECTED MIXED PLASTICS	PLASTIC‐COATED (LAMINATED) PAPER AND PAPERBOARD (COMPOSITE BOARD) / PVC / WASTE POLYMER ETHERS AND NON‐HAZARDOUS MONOMER ETHERS INCAPABLE OF FORMING PEROXIDES / GROUND PLASTICS (E.G. DEGASSED PU FOAM) THAT HAVE BEEN USED AS AN ABSORBENT FOR OIL AND HAZARDOUS CHEMICALS AND ARE THEREFORE CONTAMINATED / PLASTIC FRACTIONS FROM PROCESSING OF ELECTRICAL AND ELECTRONIC EQUIPMENT / EMPTIED PLASTIC PACKAGES THAT CONTAINED SUBSTANCES AND PREPARATIONS THAT UNDER CHEMICALS LAWS ARE REQUIRED TO BE MARKED WITH THE HAZARD SYMBOL “E” (EXPLOSIVE) / CLEAN AGRICULTURAL PLASTICS CONTAMINATED WITH STRAW OR SOIL ETC. / PLASTIC FOAM CONTAINING FULLY OR PARTIALLY HALOGENATED CFCS / FRAGMENTS OF POLYPROPYLENE‐LEAD‐ACID BATTERY CASES, TO THE EXTENT NOT CLEANED / POLYURETHANE (PU) FOAM INSULATING WASTE (E.G. FROM REFRIGERATORS) OR OTHER PU FOAM THAT WAS FOAMED WITH CFC OR WITH HCFC, HFC OR FLUOROCARBONS / PMMA VARNISH / RESINS THAT ARE NOT FULLY CURED / WASTE PLASTIC OR RESIN WITH HAZARDOUS CONTAMINATION / METALS, WOOD, OTHER CONTAMINANTS
PACKING / (*) SEE NOTE	BALES / BIGBAGS / BULK / DENSITY >= 350 KG/M3	LIQUID / SEMI-LIQUID / DENSITY < 350 KG/M3
SIZE OF INDIVIDUAL PLASTICS PIECES / (*) SEE NOTE	10 CM +/- 20%	ALL OTHER SIZES
LOWER HEATING VALUE	>= 24 MJ/KG	< 24 MJ/KG
MOISTURE	<= 15%	> 15%
ASHES	<= 25%	> 25%
CHLORINE	< 0.75%	>= 0.75%
ANTIMONY / ARSENIC / LEAD / CADMIUM / CHROME / COBALT / COPPER / MANGANESE / MERCURY / NICHEL / TALLIUM / VANADIUM / TIN / ZINC	WITHIN THE LIMITS OF / EU REG 1357/2014 AND 1272/2008	ABOVE THE LIMITS OF EU REG 1357/2014 AND 1272/2008
OTHER	NOT SMELLY, NOT DUSTY, NOT DRIPPING	SMELLY, DUSTY, DRIPPING

(*) NOTE: AS AN EXCEPTION TO FORM FACTOR, DIMENSIONAL AND SIZE CRITERIA, SOME MATERIALS CAN BE ACCEPTED WHEN THEY ARE FULLY RECOGNIZABLE AND HOMOGENEOUS. MUST BE EVALUATED CASE BY CASE.